## Slide 1: Sequential-Circuit Building Blocks
ECE 448
Lecture 4
Constants & Packages
Mixing Description Styles

## Slide 2: Reading
P. Chu, FPGA Prototyping by VHDL Examples
  Chapter 4, Regular Sequential Circuit
S. Brown and Z. Vranesic, Fundamentals of Digital Logic with VHDL Design
  Chapter 7, Flip-Flops, Registers, Counters,
  and a Simple Processor
Required
Recommended

## Slide 3
Behavioral Design Style:
Registers & Counters

## Slide 4: VHDL Description Styles
Components and
interconnects
structural
VHDL Description
Styles
dataflow
Concurrent
statements
behavioral
Registers
Shift registers
Counters
State machines
Sequential statements
and more
if you are careful
synthesizable

## Slide 5: Processes in VHDL
Processes Describe Sequential Behavior
Processes in VHDL Are Very Powerful Statements
  Allow to define an arbitrary behavior that may be difficult to represent by a real circuit
  Not every process can be synthesized
Use Processes with Caution in the Code to Be Synthesized
Use Processes Freely in Testbenches

## Slide 6: Anatomy of a Process
[label:] PROCESS [(sensitivity list)]
[declaration part]
BEGIN
statement part
END PROCESS [label];
OPTIONAL

## Slide 7: PROCESS with a SENSITIVITY LIST
List of signals to which the process is sensitive.
Whenever there is an event on any of the signals in the sensitivity list, the process fires.
Every time the process fires, it will run in its entirety.
WAIT statements are NOT ALLOWED in a processes with SENSITIVITY LIST.
label: process (sensitivity list)
declaration part
begin
statement part
end process;

## Slide 8: Component Equivalent of a Process
All signals which appear on the left of signal assignment statement (<=) are outputs e.g. y, z
All signals which appear on the sensitivity list are inputs e.g. clk
All signals which appear on the right of signal assignment statement (<=) or in logic expressions are inputs e.g. w, a, b, c
Note that not all inputs need to be included on the sensitivity list
priority: PROCESS (clk)
BEGIN
IF w(3) = '1' THEN
y <= "11" ;
ELSIF w(2) = '1' THEN
y <= "10" ;
ELSIF w(1) = c THEN
y <= a and b;
ELSE
z <= "00" ;
END IF ;
END PROCESS ;
w
a
y
z
priority
b
c
clk

## Slide 9
Registers

## Slide 10
Clock
D
0
1
1
–
0
1
0
1
Truth table
Graphical symbol
t
1
t
2
t
3
t
4
Time
Clock
D
Q
Timing diagram
Q(t+1)
Q(t)
D latch
D
Q
Clock

## Slide 11
Clk
D


0
1
0
1
Truth table
t
1
t
2
t
3
t
4
Time
Clock
D
Q
Timing diagram
Q(t+1)
Q(t)
D flip-flop
D
Q
Clock
Graphical symbol
0
–
Q(t)
1
–

## Slide 12
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY latch IS
PORT ( D, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC) ;
END latch ;
ARCHITECTURE behavioral OF latch IS
BEGIN
PROCESS ( D, Clock )
BEGIN
IF Clock = '1' THEN
Q <= D ;
END IF ;
END PROCESS ;
END behavioral;
D latch
D
Q
Clock

## Slide 13
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY flipflop IS
PORT ( D, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC) ;
END flipflop ;
ARCHITECTURE behavioral OF flipflop IS
BEGIN
PROCESS ( Clock )
BEGIN
IF rising_edge(Clock) THEN
Q <= D ;
END IF ;
END PROCESS ;
END behavioral;
D flip-flop
D
Q
Clock

## Slide 14
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY flipflop IS
PORT ( D, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC) ;
END flipflop ;
ARCHITECTURE behavioral2 OF flipflop IS
BEGIN
PROCESS ( Clock )
BEGIN
IF Clock'EVENT AND Clock = '1' THEN
Q <= D ;
END IF ;
END PROCESS ;
END behavioral2 ;
D flip-flop
D
Q
Clock

## Slide 15
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY flipflop_ar IS
PORT ( D, Reset, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC) ;
END flipflop_ar ;
ARCHITECTURE behavioral OF flipflop_ar IS
BEGIN
PROCESS ( Reset, Clock )
BEGIN
IF Reset = '1' THEN
Q <= '0' ;
ELSIF rising_edge(Clock) THEN
Q <= D ;
END IF ;
END PROCESS ;
END behavioral ;
D flip-flop with asynchronous reset
D
Q
Clock
Reset

## Slide 16
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY flipflop_sr IS
PORT ( D, Reset, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC) ;
END flipflop_sr ;
ARCHITECTURE behavioral OF flipflop_sr IS
BEGIN
PROCESS(Clock)
BEGIN
IF rising_edge(Clock) THEN
    IF Reset = '1' THEN
    Q <= '0' ;
    ELSE
    Q <= D ;
    END IF ;
    END IF;
END PROCESS ;
END behavioral ;
D flip-flop with synchronous reset
D
Q
Clock
Reset

## Slide 17: Asychronous vs. Synchronous
In the IF loop, asynchronous items are
  Before the rising_edge(Clock) statement
In the IF loop, synchronous items are
  After the rising_edge(Clock) statement

## Slide 18
8-bit register with asynchronous reset
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY reg8 IS
PORT ( D : IN STD_LOGIC_VECTOR(7 DOWNTO 0) ;
Reset, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR(7 DOWNTO 0) ) ;
END reg8 ;
ARCHITECTURE behavioral OF reg8 IS
BEGIN
PROCESS ( Reset, Clock )
BEGIN
IF Reset = '1' THEN
Q <= "00000000" ;
ELSIF rising_edge(Clock) THEN
Q <= D ;
END IF ;
END PROCESS ;
END behavioral ;`
Reset
Clock
reg8
8
8
D
Q

## Slide 19
N-bit register with asynchronous reset
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY regn IS
GENERIC ( N : INTEGER := 16 ) ;
PORT ( D : IN STD_LOGIC_VECTOR(N-1 DOWNTO 0) ;
Reset, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR(N-1 DOWNTO 0) ) ;
END regn ;
ARCHITECTURE behavioral OF regn IS
BEGIN
PROCESS ( Reset, Clock )
BEGIN
IF Reset = '1' THEN
Q <= (OTHERS => '0') ;
ELSIF rising_edge(Clock) THEN
Q <= D ;
END IF ;
END PROCESS ;
END behavioral ;
Reset
Clock
regn
N
N
D
Q

## Slide 20: A word on generics
Generics are typically integer values
  In this class, the entity inputs and outputs should be std_logic or std_logic_vector
  But the generics can be integer
Generics are given a default value
  GENERIC ( N : INTEGER := 16 ) ;
  This value can be overwritten when entity is instantiated as a component
Generics are very useful when instantiating an often-used component
  Need an 8-bit register in one place, and 16-bit register in another
  Can use the same generic code, just configure them differently

## Slide 21
Use of OTHERS
OTHERS stand for any index value that has
not been previously mentioned.
Q <= “00000001” can be written as Q <= (0 => ‘1’, OTHERS => ‘0’)
Q <= “10000001” can be written as Q <= (7 => ‘1’, 0 => ‘1’, OTHERS => ‘0’)
or Q <= (7 | 0 => ‘1’, OTHERS => ‘0’)
Q <= “00011110” can be written as Q <= (4 downto 1=> ‘1’, OTHERS => ‘0’)

## Slide 22: Component Instantiation in VHDL-93
U1: ENTITY work.regn(behavioral)
GENERIC MAP (N => 4)
PORT MAP (D => z ,
Reset => reset ,
Clock => clk,
Q => t );

## Slide 23: Component Instantiation in VHDL-87
U1: regn GENERIC MAP (N => 4)
PORT MAP (D => z ,
Reset => reset ,
Clock => clk,
Q => t );

## Slide 24
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY regne IS
GENERIC ( N : INTEGER := 8 ) ;
PORT ( D : IN STD_LOGIC_VECTOR(N-1 DOWNTO 0) ;
Enable, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR(N-1 DOWNTO 0) ) ;
END regne ;
ARCHITECTURE behavioral OF regne IS
BEGIN
PROCESS (Clock)
BEGIN
IF rising_edge(Clock) THEN
IF Enable = '1' THEN
Q <= D ;
END IF ;
END IF;
END PROCESS ;
END behavioral ;
N-bit register with enable
Q
D
Enable
Clock
regn
N
N

## Slide 25
Implementing two registers in a single process
Q
D
En
Reset
Enf
Clk
Cout_tmp
Cout
Q
D
En
Reset
Enf
Clk
V_tmp
V

## Slide 26
PROCESS (Clk, Reset)
BEGIN
IF Reset= '1' THEN
Cout <= '0';
V <= '0';
ELSIF rising_edge(Clk) THEN
IF Enf = '1' THEN
Cout <= Cout_tmp ;
V <= V_tmp;
END IF ;
END IF;
END PROCESS ;
Implementing two registers in a single process

## Slide 27
Implementing two registers in a single process
Q
D
En
Reset
EnC
Clk
Cout_tmp
Cout
Q
D
En
Reset
EnV
Clk
V_tmp
V

## Slide 28
PROCESS (Clk, Reset)
BEGIN
IF Reset = '1' THEN
Cout <= ‘0’;
V <= '0';
ELSIF rising_edge(Clk) THEN
IF EnC = '1' THEN
Cout <= Cout_tmp ;
END IF ;
IF EnV = '1' THEN
V <= V_tmp;
END IF ;
END IF;
END PROCESS ;
Implementing two registers in a single process

## Slide 29
Counters

## Slide 30
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
USE ieee.numeric_std.all ;
ENTITY upcount IS
PORT ( Clear, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR(1 DOWNTO 0) ) ;
END upcount ;
ARCHITECTURE behavioral OF upcount IS
SIGNAL Count : unsigned(1 DOWNTO 0);
BEGIN
upcount: PROCESS ( Clock )
BEGIN
IF rising_edge(Clock) THEN
IF Clear = '1' THEN
Count <= "00" ;
ELSE
Count <= Count + 1 ;
END IF ;
END IF;
END PROCESS;
Q <= std_logic_vector(Count);
END behavioral;
2-bit up-counter with synchronous reset
Q
Clear
Clock
upcount
2

## Slide 31
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
USE ieee.numeric_std.all ;
ENTITY upcount_ar IS
PORT ( Clock, Resetn, Enable : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR (3 DOWNTO 0)) ;
END upcount_ar ;
4-bit up-counter with asynchronous reset (1)
Q
Enable
Clock
upcount
4
Resetn

## Slide 32
ARCHITECTURE behavioral OF upcount _ar IS
SIGNAL Count : UNSIGNED (3 DOWNTO 0) ;
BEGIN
PROCESS ( Clock, Resetn )
BEGIN
IF Resetn = '0' THEN
Count <= "0000" ;
ELSIF rising_edge(Clock) THEN
IF Enable = '1' THEN
Count <= Count + 1 ;
END IF ;
END IF ;
END PROCESS ;
Q <= std_logic_vector(Count) ;
END behavioral ;
4-bit up-counter with asynchronous reset (2)
Q
Enable
Clock
upcount
4
Resetn

## Slide 33
Shift Registers

## Slide 34: Shift register – internal structure
D
Q
Sin
Clock
D
Q
D
Q
D
Q
Q(3)
Q(2)
Q(1)
Q(0)
Enable

## Slide 35: Shift Register With Parallel Load
D(3)
D
Q
Clock
Enable
Sin
D(2)
D
Q
D(1)
D
Q
D(0)
D
Q
Q(0)
Q(1)
Q(2)
Q(3)
Load

## Slide 36
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY shift4 IS
PORT ( D : IN STD_LOGIC_VECTOR(3 DOWNTO 0) ;
Enable : IN STD_LOGIC ;
Load : IN STD_LOGIC ;
Sin : IN STD_LOGIC ;
Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR(3 DOWNTO 0) ) ;
END shift4 ;
4-bit shift register with parallel load (1)
Q
Enable
Clock
shift4
4
D
Load
Sin
4

## Slide 37
ARCHITECTURE behavioral OF shift4 IS
SIGNAL Qt : STD_LOGIC_VECTOR(3 DOWNTO 0);
BEGIN
PROCESS (Clock)
BEGIN
IF rising_edge(Clock) THEN
IF Enable = ‘1’ THEN
IF Load = '1' THEN
Qt <= D ;
ELSE
Qt <= Sin & Qt(3 downto 1);
END IF ;
END IF;
END IF ;
END PROCESS ;
Q <= Qt;
END behavioral ;
4-bit shift register with parallel load (2)
Q
Enable
Clock
shift4
4
D
Load
Sin
4

## Slide 38
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY shiftn IS
GENERIC ( N : INTEGER := 8 ) ;
PORT ( D : IN STD_LOGIC_VECTOR(N-1 DOWNTO 0) ;
Enable : IN STD_LOGIC ;
Load : IN STD_LOGIC ;
Sin : IN STD_LOGIC ;
Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR(N-1 DOWNTO 0) ) ;
END shiftn ;
N-bit shift register with parallel load (1)
Q
Enable
Clock
shiftn
N
D
Load
Sin
N

## Slide 39
ARCHITECTURE behavioral OF shiftn IS
SIGNAL Qt: STD_LOGIC_VECTOR(N-1 DOWNTO 0);
BEGIN
PROCESS (Clock)
BEGIN
IF rising_edge(Clock) THEN
IF Enable = ‘1’ THEN
IF Load = '1' THEN
Qt <= D ;
ELSE
Qt <= Sin & Qt(N-1 downto 1);
END IF ;
END IF;
END IF ;
END PROCESS ;
Q <= Qt;
END behavior al;
N-bit shift register with parallel load (2)
Q
Enable
Clock
shiftn
N
D
Load
Sin
N

## Slide 40
Generic Component Instantiation

## Slide 41
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY regne IS
GENERIC ( N : INTEGER := 8 ) ;
PORT ( D : IN STD_LOGIC_VECTOR(N-1 DOWNTO 0) ;
Enable, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR(N-1 DOWNTO 0) ) ;
END regne ;
ARCHITECTURE Behavior OF regne IS
BEGIN
PROCESS (Clock)
BEGIN
IF (Clock'EVENT AND Clock = '1' ) THEN
IF Enable = '1' THEN
Q <= D ;
END IF ;
END IF;
END PROCESS ;
END Behavior ;
N-bit register with enable
Q
D
Enable
Clock
regne
N
N

## Slide 42: Circuit built of medium scale components
w
0
w
3
y
1
y
0
z
w
1
w
2
w
1
En
y
3
w
0
y
2
y
1
y
0
s(0)
0
1
s(1)
0
1
r(0)
r(1)
r(2)
r(3)
r(4)
r(5)
p(0)
p(1)
p(2)
p(3)
q(1)
q(0)
ena
z(3)
z(2)
z(1)
z(0)
dec2to4
priority
t(3)
t(2)
t(1)
t(0)
regne
D
Q
Clk
Clock
Enable
En

## Slide 43: Structural description – example (1) VHDL-93
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY priority_resolver IS
PORT (r : IN STD_LOGIC_VECTOR(5 DOWNTO 0) ;
s : IN STD_LOGIC_VECTOR(1 DOWNTO 0) ;
clk : IN STD_LOGIC;
en : IN STD_LOGIC;
t : OUT STD_LOGIC_VECTOR(3 DOWNTO 0) ) ;
END priority_resolver;
ARCHITECTURE structural OF priority_resolver IS
SIGNAL p : STD_LOGIC_VECTOR (3 DOWNTO 0) ;
SIGNAL q : STD_LOGIC_VECTOR (1 DOWNTO 0) ;
SIGNAL z : STD_LOGIC_VECTOR (3 DOWNTO 0) ;
SIGNAL ena : STD_LOGIC ;

## Slide 44: Structural description – example (2) VHDL-93
BEGIN
u1: ENTITY work.mux2to1(dataflow)
PORT MAP (w0 => r(0) ,
w1 => r(1),
s => s(0),
f => p(0));
p(1) <= r(2);
p(2) <= r(3);
u2: ENTITY work.mux2to1(dataflow)
PORT MAP (w0 => r(4) ,
w1 => r(5),
s => s(1),
f => p(3));
u3: ENTITY work.priority(dataflow)
PORT MAP (w => p,
y => q,
z => ena);

## Slide 45: Structural description – example (3) VHDL-93
u4: ENTITY work.dec2to4 (dataflow)
PORT MAP (w => q,
En => ena,
y => z);
u5: ENTITY work.regne(behavioral)
GENERIC MAP (N => 4)
PORT MAP (D => z ,
Enable => En ,
Clock => Clk,
Q => t );
END structural;

## Slide 46: Structural description – example (1) VHDL-87
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY priority_resolver IS
PORT (r : IN STD_LOGIC_VECTOR(5 DOWNTO 0) ;
s : IN STD_LOGIC_VECTOR(1 DOWNTO 0) ;
clk : IN STD_LOGIC;
en : IN STD_LOGIC;
t : OUT STD_LOGIC_VECTOR(3 DOWNTO 0) ) ;
END priority_resolver;
ARCHITECTURE structural OF priority_resolver IS
SIGNAL p : STD_LOGIC_VECTOR (3 DOWNTO 0) ;
SIGNAL q : STD_LOGIC_VECTOR (1 DOWNTO 0) ;
SIGNAL z : STD_LOGIC_VECTOR (3 DOWNTO 0) ;
SIGNAL ena : STD_LOGIC ;

## Slide 47: Structural description – example (2) VHDL-87
COMPONENT mux2to1
PORT (w0, w1, s : IN STD_LOGIC ;
f : OUT STD_LOGIC ) ;
END COMPONENT ;
COMPONENT priority
PORT (w : IN STD_LOGIC_VECTOR(3 DOWNTO 0) ;
y : OUT STD_LOGIC_VECTOR(1 DOWNTO 0) ;
z : OUT STD_LOGIC ) ;
END COMPONENT ;
COMPONENT dec2to4
PORT (w : IN STD_LOGIC_VECTOR(1 DOWNTO 0) ;
En : IN STD_LOGIC ;
y : OUT STD_LOGIC_VECTOR(3 DOWNTO 0) ) ;
END COMPONENT ;

## Slide 48: Structural description – example (3) VHDL-87
COMPONENT regne
GENERIC ( N : INTEGER := 8 ) ;
PORT ( D : IN STD_LOGIC_VECTOR(N-1 DOWNTO 0) ;
Enable, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR(N-1 DOWNTO 0) ) ;
END COMPONENT ;

## Slide 49: Structural description – example (4) VHDL-87
BEGIN
u1: mux2to1 PORT MAP (w0 => r(0) ,
w1 => r(1),
s => s(0),
f => p(0));
p(1) <= r(2);
p(2) <= r(3);
u2: mux2to1 PORT MAP (w0 => r(4) ,
w1 => r(5),
s => s(1),
f => p(3));
u3: priority PORT MAP (w => p,
y => q,
z => ena);
u4: dec2to4 PORT MAP (w => q,
En => ena,
y => z);

## Slide 50: Structural description – example (5) VHDL-87
u5: regne GENERIC MAP (N => 4)
PORT MAP (D => z ,
Enable => En ,
Clock => Clk,
Q => t );
END structural;

## Slide 51
Constants

## Slide 52: Constants
Syntax:
CONSTANT name : type := value;
Examples:
CONSTANT init_value : STD_LOGIC_VECTOR(3 downto 0) := "0100";
CONSTANT ANDA_EXT : STD_LOGIC_VECTOR(7 downto 0) := X"B4";
CONSTANT counter_width : INTEGER := 16;
CONSTANT buffer_address : INTEGER := 16#FFFE#;
CONSTANT clk_period : TIME := 20 ns;
CONSTANT strobe_period : TIME := 333.333 ms;

## Slide 53: Constants - features
Constants can be declared in a
PACKAGE, ARCHITECTURE, ENTITY
When declared in a PACKAGE, the constant
is truly global, for the package can be used
in several entities.
When declared in an ARCHITECTURE, the
constant is local, i.e., it is visible only within this architecture.
When declared in an ENTITY declaration, the constant
can be used in all architectures associated with this entity.

## Slide 54: Example of package
library ieee;
use ieee.std_logic_1164.all;
package alu_pkg is
constant OPCODE_NOR : std_logic_vector(2 downto 0) := "000";
constant OPCODE_NAND : std_logic_vector(2 downto 0) := "001";
constant OPCODE_XOR : std_logic_vector(2 downto 0) := "010";
constant OPCODE_UADD : std_logic_vector(2 downto 0) := "011";
constant OPCODE_SADD : std_logic_vector(2 downto 0) := "100";
constant OPCODE_SSUB : std_logic_vector(2 downto 0) := "101";
constant OPCODE_UMUL : std_logic_vector(2 downto 0) := "110";
constant OPCODE_SMUL : std_logic_vector(2 downto 0) := "111";
end alu_pkg;

## Slide 55: Using objects from a package
library ieee;
use ieee.std_logic_1164.all;
library work;
use work.alu_pkg.all;
entity alu_comb is
…………..

## Slide 56
Mixing Description Styles
Inside of an Architecture

## Slide 57: VHDL Description Styles
Components and
interconnects
structural
VHDL Description
Styles
dataflow
Concurrent
statements
behavioral
Registers
Shift registers
Counters
State machines
Sequential statements
synthesizable

## Slide 58: Mixed Style Modeling
  architecture ARCHITECTURE_NAME of ENTITY_NAME is
  Here you can declare signals, constants, types, etc.
  begin
  Concurrent statements:
    Simple signal assignment
    Conditional signal assignment
    Selected signal assignment
    Component instantiation statement
    Process statement
      inside process you can use only sequential statements
  end ARCHITECTURE_NAME;

## Slide 59: PRNG Example (1)
library IEEE;
use IEEE.STD_LOGIC_1164.all;
use work.prng_pkg.all;
ENTITY PRNG IS
PORT( Coeff : in std_logic_vector(4 downto 0);
Load_Coeff : in std_logic;
Seed : in std_logic_vector(4 downto 0);
Init_Run : in std_logic;
Clk : in std_logic;
Current_State : out std_logic_vector(4 downto 0));
END PRNG;
ARCHITECTURE mixed OF PRNG is
signal Ands : std_logic_vector(4 downto 0);
signal Sin : std_logic;
signal Coeff_Q : std_logic_vector(4 downto 0);
signal Shift5_Q : std_logic_vector(4 downto 0);

## Slide 60: PRNG Example (2)
BEGIN
-- Data Flow
Sin <= Ands(0) XOR Ands(1) XOR Ands(2) XOR Ands(3) XOR Ands(4);
Current_State <= Shift5_Q;
Ands <= Coeff_Q AND Shift5_Q;
-- Behavioral
Coeff_Reg: PROCESS(Clk)
BEGIN
IF rising_edge(Clk) THEN
IF Load_Coeff = '1' THEN
Coeff_Q <= Coeff;
END IF;
END IF;
END PROCESS;
-- Structural
Shift5_Reg : ENTITY work.Shift5(behavioral) PORT MAP ( D => Seed,
Load => Init_Run,
Sin => Sin,
Clock => Clk,
Q => Shift5_Q);
END mixed;

## Slide 61
Sequential Logic Synthesis
for
Beginners

## Slide 62: For Beginners
Use processes with very simple structure only
to describe
- registers
- shift registers
- counters
- state machines.
Use examples discussed in class as a template.
Create generic entities for registers, shift registers, and
counters, and instantiate the corresponding components in
a higher level circuit using GENERIC MAP PORT MAP.
Supplement sequential components with
combinational logic described using concurrent statements.

## Slide 63
Sequential Logic Synthesis
for
Intermediates

## Slide 64: For Intermmediates
Use Processes with IF and CASE statements only. Do not use LOOPS or VARIABLES.
Sensitivity list of the PROCESS should include only signals that can by themsleves change the outputs of the sequential circuit (typically, clock and asynchronous set or reset)
Do not use PROCESSes without sensitivity list
(they can be synthesizable, but make simulation inefficient)

## Slide 65: For Intermmediates (2)
Given a single signal, the assignments to this signal should
only be made within a single process block in order to avoid
possible conflicts in assigning values to this signal.
Process 1: PROCESS (a, b)
BEGIN
y <= a AND b;
END PROCESS;
Process 2: PROCESS (a, b)
BEGIN
y <= a OR b;
END PROCESS;

## Slide 66
Non-synthesizable VHDL

## Slide 67: Delays
Delays are not synthesizable
Statements, such as
wait for 5 ns
a <= b after 10 ns
will not produce the required delay, and
should not be used in the code intended
for synthesis.

## Slide 68: Initializations
Declarations of signals (and variables)
with initialized values, such as
SIGNAL a : STD_LOGIC := ‘0’;
cannot be synthesized, and thus should
be avoided.
If present, they will be ignored by the
synthesis tools.
Use set and reset signals instead.

## Slide 69: Dual-edge triggered register/counter (1)
In FPGAs register/counter can change only
at either rising (default) or falling edge of the
clock.
Dual-edge triggered clock is not synthesizable
correctly, using either of the descriptions
provided below.

## Slide 70: Dual-edge triggered register/counter (2)
PROCESS (clk)
BEGIN
IF (clk’EVENT AND clk=‘1’ ) THEN
counter <= counter + 1;
ELSIF (clk’EVENT AND clk=‘0’ ) THEN
counter <= counter + 1;
END IF;
END PROCESS;

## Slide 71: Dual-edge triggered register/counter (3)
PROCESS (clk)
BEGIN
IF (clk’EVENT) THEN
counter <= counter + 1;
END IF;
END PROCESS;
PROCESS (clk)
BEGIN
counter <= counter + 1;
END PROCESS;