## Slide 1: FPGA Internal Structures
System on Chip Parviz Keshavarzi
2020

## Slide 2
Rabaey, Chandrakasan and Nikolic “Digital Integrated Circuits A Design Perspective “, 2002
Haibo Wang, ECE 428 Programmable ASIC Design
ECE Department, Southern Illinois University

## Slide 4: A Historical Perspective: the PLA
x
0
x
1
x
2
AND
plane
x
0
x
1
x
2
Product terms
OR
plane
f
0
f
1

## Slide 5: Two-Level Logic
Inverting format (NOR-NOR) more effective
Every logic function can be expressed in sum-of-products format (AND-OR)
minterm

## Slide 6: PLA Layout – Exploiting Regularity
V
DD
GND
f
And-Plane
Or-Plane

## Slide 7: Breathing Some New Life in PLAs
River PLAs
A cascade of multiple-output PLAs.
Adjacent PLAs are connected via river routing.
No placement and routing needed.
Output buffers and the input buffers of the next stage are shared.
Courtesy B. Brayton

## Slide 9
FPGA
FPGA consists of an array of programmable basic logic cells surrounded by programmable interconnect.
FPGA Structure
Logic cell
Programmable
interconnect
I/O Cell

## Slide 10: Field-Programmable Gate Arrays
Logic blocks
  to implement combinational and sequential logic
Interconnect
  wires to connect inputs and outputs to logic blocks
I/O blocks
  special logic blocks at periphery of device for external connections
Key questions:
  how to make logic blocks programmable?
  how to connect the wires?
  after the chip has been fabbed

## Slide 11: 2-input MUX as programmable logic block
F
A
0
B
S
1
Configuration
A
B
S
F=
0
0
0
0
0
X
1
X
0
Y
1
Y
0
Y
X
XY
X
0
Y
Y
0
X
Y
1
X
X
+
Y
1
0
X
1
0
Y
1
1
1
1
XY
XY
X
Y

## Slide 12: Implementing Logic functions with LUTs
Each logic block in an FPGA has a small number of inputs and outputs
The most commonly used logic block is a lookup table (LUT), which contains storage cells that are used to implement a small logic function

## Slide 13: Two-input LUT

## Slide 14: LUT-Based Logic Cell
Out
ln1
ln2
Memory
In
Out
00
0
01
1
10
1
11
0

## Slide 15: 2-input mux as programmable logic block
F
A
0
B
S
1
Configuration
A
B
S
F=
0
0
0
0
0
X
1
X
0
Y
1
Y
0
Y
X
XY
X
0
Y
Y
0
X
Y
1
X
X
1
Y
1
0
X
1
0
Y
1
1
1
1
XY
XY
X
Y

## Slide 16: Logic Cell of Actel Fuse-Based FPGA

## Slide 17: Look-up Table Based Logic Cell

## Slide 18: LUT-Based Logic Cell
Courtesy Xilinx
D
4
C
1
....C
4
x
xxxxx
D
3
D
2
D
1
F
4
F
3
F
2
F
1
Logic
function
of
xxx
Logic
function
of
xxx
Logic
function
of
xxx
xx
xx
4
xx
xx
xx
xx
xx
xx
xx
x
x
x
xxxx
xxxx
xxxx
H
P
Bits
control
Bits
control
Multiplexer Controlled
by Configuration Program
x
x
x
x
xx
x
xx
xx
xxxx
x
xx
xxxx
xx
x
xx
x
xx
xx
Xilinx 4000 Series
Figure must be
updated

## Slide 19: Array-Based Programmable Wiring
Input/output pin
Programmed interconnection
Interconnect
Point
Horizontal
tracks
Vertical tracks
Cell

## Slide 20: Mesh-based Interconnect Network
Switch Box
Connect Box
Interconnect Point
Courtesy Dehon and Wawrzyniek

## Slide 21: Transistor Implementation of Mesh
Courtesy Dehon and Wawrzyniek

## Slide 22: Hierarchical Mesh Network
Use overlayed mesh
to support longer connections
Reduced fanout and reduced resistance
Courtesy Dehon and Wawrzyniek

## Slide 23: Field-Programmable Gate Arrays Fuse-based
Standard-cell like
floorplan

## Slide 24: Xilinx 4000 Interconnect Architecture
2
12
8
4
3
2
3
CLB
8
4
8
4
Quad
Single
Double
Long
Direct
Connect
Direct
Connect
Quad
Long
Global
Clock
Long
Double
Single
Global
Clock
Carry
Chain
Long
12
4
4
Courtesy Xilinx

## Slide 25: Field-Programmable Gate Arrays
Logic blocks
  to implement combinational and sequential logic
Interconnect
  wires to connect inputs and outputs to logic blocks
I/O blocks
  special logic blocks at periphery of device for external connections
Key questions:
  how to make logic blocks programmable?
  how to connect the wires?
  after the chip has been fabbed

## Slide 26: Xilinx Programmable Gate Arrays
CLB - Configurable Logic Block
  5-input, 1 output function
  or 2 4-input, 1 output functions
  optional register on outputs
Built-in fast carry logic
Can be used as memory
Three types of routing
  direct
  general-purpose
  long lines of various lengths
RAM-programmable
  can be reconfigured