## Slide 1: FPGA CPLD Internal Structures
System on Chip Parviz Keshavarzi
2017

## Slide 2
Rabaey, Chandrakasan and Nikolic “Digital Integrated Circuits A Design Perspective “, 2002
Haibo Wang, ECE 428 Programmable ASIC Design
ECE Department, Southern Illinois University

## Slide 3
ASIC Design vs FPGA Design

## Slide 4: Implementation Choices
Custom
Standard Cells
Compiled Cells
Ma
cro Cells
Cell-based
Pre-diffused
(Gate Arrays)
Pre-wired
(FPGAs)
Array-based
Semicustom
Digital Circuit Implementation Approaches

## Slide 5
FPGA v.s. CPLD
Capacitance
 | SPLDs | CPLDs | FPGAs
Equivalent gates | 0 ~ 200 | 200 ~ 12,000 | 1000 ~ 1,000,000
Applications
CPLDs
FPGAs
Implement random glue logics or Replace circuits previously implemented by multiple SPLDs
Circuits that can exploit wide AND/OR gates, and do not need a very large number of flip-flops are good candidates for implementation in CPLDs.
FPGAs can be used in various applications: prototyping, FPGA-based computers, on-site hardware re-configuration, DSP, logic emulation, network components, etc.

## Slide 6: Cell-based Design (or standard cells)
Routing channel
requirements are
reduced by presence
of more interconnect
layers

## Slide 7: Standard Cell - Example
3-input NAND cell
(from ST Microelectronics):
C = Load capacitance
T = input rise/fall time

## Slide 8: Late-Binding Implementation
Pre-diffused
(Gate Arrays)
Pre-wired
(FPGAs)
Array-based

## Slide 9
PLA
Programmable AND Plane
X
Y
O1
O2
O3
O4
Programmable Node
Programmable OR Plane
Connect
Disconnect
X
X
Y
Y
X
Y
XY
XY
XY
XY
Un-programmed

## Slide 10
PLA
Programmable AND Plane
Programmable OR Plane
X
Y
Z
XY+YZ
?
?
XZ+XYZ
YZ
XZ
XYZ
XY

## Slide 11
PAL
Programmable AND Plane
X
Y
O1
O2
O3
O4
Fix OR Plane

## Slide 12
PAL with Logic Expanders
Programmable AND Plane
Logic expanders
Fix OR Plane
?

## Slide 13
PLA v.s. PAL
PLAs are more flexible than PALs since both AND & OR planes are programmable in PLAs.
Because both AND & OR planes are programmable, PLAs are expensive to fabricate and have large propagation delay.
By using fix OR gates, PALs are cheaper and faster than PLAs.
Logic expanders increase the flexibilities of PALs, but result in significant propagation delay.
PALs usually contain D flip-flops connected to the outputs of OR gates to implement sequential circuits.
PLAs and PALs are usually referred to as SPLD.

## Slide 14: Array-Based Programmable Logic
PLA
PROM
PAL
I
5
I
4
O
0
I
3
I
2
I
1
I
0
O
1
O
2
O
3
Programmable AND array
Programmable
OR array
I
5
I
4
O
0
I
3
I
2
I
1
I
0
O
1
O
2
O
3
Programmable AND array
Fixed OR array
Indicates programmable connection
Indicates fixed connection
O
0
I
3
I
2
I
1
I
0
O
1
O
2
O
3
Fixed AND array
Programmable
OR array

## Slide 15: Implementing functions with PLA

## Slide 16: Programming a PROM
f
0
1
X
2
X
1
X
0
f
1
NA
NA
: programmed node

## Slide 17: PAL 16R8

## Slide 18: More Complex PAL
Higher capacity devices
Single PAL architecture is not feasible
Programmable logic planes grow too quickly
Complex Programmable Logic Device (CPLD)
Multiple PALs integrated together

## Slide 19: CPLD

## Slide 20
CPLD
A CPLD comprises multiple PAL-like blocks on a single chip with programmable interconnect to connect the blocks.
CPLD Architecture
PAL-like
block
PAL-like
block
PAL-like
block
PAL-like
block
I/O block
I/O block
I/O block
I/O block
Programmable interconnect

## Slide 21: More Complex PAL
From Smith97
i inputs, j minterms/macrocell, k macrocells

## Slide 22
Altera MAX CPLD
LAB
LAB
LAB
LAB
LAB
LAB
I/O Cell
Chip-wide
interconnect
Altera MAX chip
LAB (Logic Array Block)
LA
(local array)
• • •
Macroccell
Each LAB contains 16 macrocells

## Slide 23
Macrocell of Altera MAX CPLD
5
114
Product term
select
Programmable
inversion
D
Q
M
Local Array
3
Clock, clear, preset, enable
System clock
System enable
Parallel expander
To next macrocell
Macrocell
MAX 9000 has 33 inputs, can you explain why LA has 114 inputs?
OUT

## Slide 24: Altera CPLD
MAX 7000
Array of Logic Array Blocks (LABs)
Programmable Interconnect Array (PIA): Array of interconnect wires
LAB I/O ←PIA→ LAB I/O
Chip I/O ↔ PIA
Chip I/O ↔ LABs

## Slide 25: MAX 7000 Macrocell

## Slide 26: AMD - CPLD
AMD Mach 4 CPLD

## Slide 27: Altera MAX Interconnect Architecture
LAB2
PIA
LAB1
LAB6
t
PIA
t
PIA
row channel
column channel
LAB
Courtesy Altera
Array-based
(MAX 3000-7000)
Mesh-based
(MAX 9000)

## Slide 28
Definitions
Programmable logic devices (PLDs)
(or Field Programmable Device (FPD)):
a general term that refers to any type of integrated circuit used for implementing digital hardware, where the chip can be configured by the end user to realize different designs. Programming of such a device often involves placing the chip into a special programming unit, but some chips can also be configured “in-system”.
Source: S. Brown and J. Rose, FPGA and CPLD Architectures: A Tutorial,
IEEE Design and Test of Computer, 1996

## Slide 29
Classifications
PLA — a Programmable Logic Array (PLA) is a relatively
small FPD that contains two levels of logic, an AND-
plane and an OR-plane, where both levels are
programmable
PAL — a Programmable Array Logic (PAL) is a relatively
small FPD that has a programmable AND-plane
followed by a fixed OR-plane
SPLD — refers to any type of Simple PLD, usually either a
PLA or PAL
CPLD — a more Complex PLD that consists of an
arrangement of multiple SPLD-like blocks on a
single chip.
FPGA — a Field-Programmable Gate Array is an FPD
featuring a general structure that allows very high
logic capacity.

## Slide 30: Late-Binding Implementation
Pre-diffused
(Gate Arrays)
Pre-wired
(FPGA's)
Array-based

## Slide 31: Prewired Arrays
Classification of prewired arrays (or field-programmable devices):
Based on Programming Technique
  Fuse-based (program-once)
  Non-volatile EPROM based
  RAM based
Programmable Logic Style
  Array-Based
  Look-up Table
Programmable Interconnect Style
  Channel-routing
  Mesh networks

## Slide 32: Programming Technologies
Fuse and anti-fuse
  fuse makes or breaks link between two wires
  typical connections are 50-300 ohm
  one-time programmable
Flash
  High density
  Process issues
RAM-based
  memory bit controls a switch that connects/disconnects two wires
  typical connections are .5K-1K ohm
  can be programmed and re-programmed easily (tested at factory)

## Slide 33: Fuse-Based FPGA
antifuse polysilicon
ONO dielectric
n
+
antifuse diffusion
2
l
From Smith97
Open by default, closed by applying current pulse

## Slide 34
FPGA
FPGA consists of an array of programmable basic logic cells surrounded by programmable interconnect.
FPGA Structure
Logic cell
Programmable
interconnect
I/O Cell

## Slide 35: Field-Programmable Gate Arrays
Logic blocks
  to implement combinational and sequential logic
Interconnect
  wires to connect inputs and outputs to logic blocks
I/O blocks
  special logic blocks at periphery of device for external connections
Key questions:
  how to make logic blocks programmable?
  how to connect the wires?
  after the chip has been fabbed

## Slide 36: FPGAs

## Slide 37: 2-input MUX as programmable logic block
F
A
0
B
S
1
Configuration
A
B
S
F=
0
0
0
0
0
X
1
X
0
Y
1
Y
0
Y
X
XY
X
0
Y
Y
0
X
Y
1
X
X
+
Y
1
0
X
1
0
Y
1
1
1
1
XY
XY
X
Y

## Slide 38: Implementing Logic functions with LUTs
Each logic block in an FPGA has a small number of inputs and outputs
The most commonly used logic block is a lookup table (LUT), which contains storage cells that are used to implement a small logic function

## Slide 39: Two-input LUT

## Slide 40: LUT-Based Logic Cell
Out
ln1
ln2
Memory
In
Out
00
0
01
1
10
1
11
0

## Slide 41: 2-input mux as programmable logic block
F
A
0
B
S
1
Configuration
A
B
S
F=
0
0
0
0
0
X
1
X
0
Y
1
Y
0
Y
X
XY
X
0
Y
Y
0
X
Y
1
X
X
1
Y
1
0
X
1
0
Y
1
1
1
1
XY
XY
X
Y

## Slide 42: Logic Cell of Actel Fuse-Based FPGA

## Slide 43: Look-up Table Based Logic Cell